## Slide 1
ONOS
Open Network Operating System
An Open-Source Distributed SDN OS
Pankaj Berde, Jonathan Hart, Masayoshi Kobayashi, Pavlin Radoslavov, Pingping Lin, Rachel Sverdlov, Suibin Zhang, William Snow, Guru Parulkar
Notes: Introduction:
Acronym ONOS -> Open Network Operating System -> Platform to open networks to realize pure SDN

## Slide 2: Software Defined Network (SDN)
Global Network Map
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Network OS
Control
Program
Control
Program
Control
Program
Abstract
Forwarding
Model
(e.g. OpenFlow)
Notes: Separate control plane and data plane.
All control functions are consolidated within one control plane.
Control plane an abstract forwarding model to talk to forwarding plane/devices and OpenFlow is that abstraction
Provide a global view of the network to control program
Each control program is a function of global network map and programs the data plane on the network map abstraction.
Network OS converts these intentions into OpenFlow forwarding rules and pushes onto the physical network.

## Slide 3: Match-Action Forwarding Abstraction
Match | Action
F | Action(F)
G | Action(G)
H | Action(H)
H
H’
Action Primitives
“Forward to ports 4 & 5”
“Push header Y after bit 12”
“Pop header bits 8-12”
“Decrement bits 13-18”
“Drop packet”
…
“Plumbing primitives”
Notes: OpenFlow provides a simple forwarding abstraction by create rules on the data plane. A packet is matched against a rule and action of the rule is determined. The packet takes the path determined by the this simple match/action rules.

## Slide 4: Software Defined Network (SDN)
Global Network Map
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Control
Program
Control
Program
Control
Program
firewall.c
…
if( TCP_port == SMTP)
dropPacket();
…
Match | Action
F | Action(F)
G | Action(G)
H | Action(H)
Match | Action
A | Action(A)
G | Action(G)
D | Action(D)
Match | Action
A | Action(A)
B | Action(B)
C | Action(C)
Match | Action
X | Action(X)
Y | Action(Y)
Z | Action(Z)
Match | Action
A | Action(A)
G | Action(G)
H | Action(H)
Network OS
Notes: A control program, say “firewall” writes a rule on the network map. The Network OS looks up all the rules on the devices. Then the NOS translates the control programs intention into appropriate match/action rules. Next it adds this rule to the forwarding table of the devices.

## Slide 5: ONOS Use Cases For Service Provider Networks
WAN core backbone
  Multiprotocol Label Switching (MPLS) with Traffic Engineering (TE)
Cellular access network
  LTE for a metro area
Metro Ethernets
  Access network for enterprises
Wired access/aggregation
  Access network for homes
  DSL/Cable
Core
Cellular
Metro
Access
Notes: ----- Meeting Notes (11/20/13 22:24) -----
The focus for ONOS has been service provider networks.
A service provider network is has a core back bone network and various access networks attached to them.
The typical WAN core backbone is programmed using MPLS and a application to allocate resources and capacity to various traffic needs is called Traffic Engineering.
Similarly the various access networks like cellular, metro or wired access network have their own characteristics and applications.
For this discussion we will drill down a bit on Traffic Engineering

## Slide 6: WAN Traffic Engineering Use Case Scenario
(*) Other configurations possible with tradeoffs: e.g., ONOS cluster per region
Single ONOS Cluster in a Data Center*
8-16 ONOS instances max for storage/compute capacity
Out-of-band connection between ONOS and Switches
O(10)ms delay
Single DC
ONOS instances
AT&T Backbone Network
Notes: ----- Meeting Notes (11/20/13 23:20) -----
This is a picture of AT&T backbone network
Here you see various metro regions are connected with high bandwidth connectivity. Lets assume that we are controlling the complete core network using a single cluster of ONOS servers. Typically we will need 8-16 servers to control similar network. ONOS controls the core switches using an out-of-band connection. Typical latency between the switch and ONOS is around 10-50 ms.

## Slide 7: WAN Traffic Engineering Use Case Scenario
Single ONOS Cluster in a Data Center*
8-16 ONOS instances max
Out-of-band connection between ONOS and Switches
O(10)ms delay
Single DC
ONOS instances
(Numbers based on Stanford Ph.D thesis (Saurav Das) and interview with Google & Global Crossing)
AT&T Backbone Network
150 Core Switches (AT&T/Global Crossing)
300 Edge Switches (AT&T/Global Crossing)
50K edge-to-edge tunnels (Global Crossing)
400K IP prefixes (current BGP table size)
Notes: ----- Meeting Notes (11/20/13 23:20) -----
Lets see some sizing information on a core backbone bases on prior research on AT&T and Global Crossing's core networks.

## Slide 8: Cellular Core Network Use Case*
Internet
Single DC
ONOS nodes
Cellular Core Network
Base
Station
Access Edge
Gateway
Edge
~1K Ues per BS
~10K flows per BS
~1 – 10 Gbps per BS
~1 million UEs
~10 million flows
~400 Gbps – 2 Tbps
Middle boxes
(firewall, IDS, etc.)
(*) Based on Jen Rexford’s study at Princeton
O(1) ms delay
~100 Switches, 1000 Base Stations
Notes: ----- Meeting Notes (11/20/13 23:20) -----
Just like the Core network we are trying to understand the control plane needs for a Cellular core network. We are working closely with Jen Rexford and her student from Princeton.
Based on their study we can show a cellular core network and how ONOS would control it. On a cellular network the end devices are shown as user agents on this network which initiate all the requests. The user agent or the end devices connect to a base station and intiates the traffic request. There are several base stations spread across the metro and these base stations aggregate into a cellular cell network which forwards the traffic out to internet on edge gateways. All the traffic eventually aggregates into these gateway edges. ONOS can control all these swtiches using a single cluster with out-of-band connection to the swtiches.
Here are some effort to size this network.

## Slide 9: ONOS: Open Network OS
Routing
TE
ONOS
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Mobility
Programmable
Base Station
Openflow
Scale-out
Design
Fault Tolerance
Global network view
Global Network View
Notes: This is a clean SDN reference architecture. There are three questions we still need to answer.
Number 1, will the Network OS become a performance bottleneck? Or can we scale the Network OS horizontally as we need more horse power?
Number 2, will the Network OS become a single point of failure? Or can we make the Network OS and the control plane fault tolerant?
The third question has to do with Northbound API. What is the best abstraction the Network OS can offer to application writers that enables reusable and pluggable network control and management applications?
ONOS attempts to address exactly these issues…

## Slide 10: Prior Work
Distributed control platform for large-scale networks
ONIX: closed source; datacenter + virtualization focus
ONOS design influenced by ONIX
Distributed:
ONIX
Single Instance
NOX, POX, Beacon, Floodlight, Trema controllers
Helios, Midonet, Hyperflow, Maestro, Kandoo, …
Community needs an open source distributed network OS
Notes: ONIX did attempt to solve these issues. There are few more efforts. To enable more research in this area community needs an open distributed NOS.

## Slide 11: ONOS Phase 1: Goals December 2012 – December 2013
Demo Key Functionality
  Fault-Tolerance: Highly Available control plane
  Scale-out: Using distributed architecture
  Global Network View: Network Graph abstraction
Non Goals
  Performance optimization
  Stress testing
Notes: Started in December with a primary goal to demonstrate we can build ONOS with scale-out distributed architecture which has high-availability and global network view as network graph.
----- Meeting Notes (11/20/13 17:23) -----
reactive flows should be dropped

## Slide 12: ONOS – Architecture Overview

## Slide 13: ONOS High Level Architecture
Host
Host
Host
Titan Graph DB
Cassandra In-Memory DHT
Instance 1
Instance 2
Instance 3
Network Graph Eventually consistent
Distributed Registry Strongly Consistent
Zookeeper
OpenFlow Controller+
OpenFlow Controller+
OpenFlow Controller+
+Floodlight Drivers
Scale-out
Coordination
Distributed Network
Graph/State
Control Application
Control Application
Applications
Notes: Built on two distributed data constructs
1> Network Graph which is the global network view containing the network state represented as a graph which is eventually consistent
2> Distributed Registry is the global cluster management state stored in Zookeeper using transactional consistency.
Multiple instances of ONOS control different parts of network and help realize a single global network view by cooperatively using these two distributed data constructs.
----- Meeting Notes (5/15/13 14:21) -----
Distribruted Registry keeps information on who is in control of the switch objects and has write permissions to update the network graph. In general it stores the resource ownership in a strongly consistent way.
----- Meeting Notes (7/29/13 12:57) -----
order animation
remove floodlight

## Slide 14: Scale-out & HA

## Slide 15: ONOS Scale-Out
Distributed Network OS
Instance 2
Instance 3
Instance 1
Network Graph
Global network view
An instance is responsible for maintaining a part of network graph
Control capacity can grow with network size or application need
Data plane
Notes: A part of network is solely controlled by a single ONOS instance and the same instance is also solely responsible for maintaining the state of the partition into the network graph.
[We also refer this as Control isolation.]
This enables simpler scale-out design.
As the network grows beyond the control capacity one can add another instance which will be responsible for a new part of network . As this part is realized into Network Graph, applications will get a global network view.
----- Meeting Notes (7/29/13 12:57) -----
Fix animation

## Slide 16: ONOS Control Plane Failover
Master
Switch A = ONOS 1
Candidates = ONOS 2, ONOS 3
Master
Switch A = ONOS 1
Candidates = ONOS 2, ONOS 3
Master
Switch A = ONOS 1
Candidates = ONOS 2, ONOS 3
Distributed Network OS
Instance 2
Instance 3
Instance 1
Distributed Registry
Host
Host
Host
A
B
C
D
E
F
Master
Switch A = NONE
Candidates = ONOS 2, ONOS 3
Master
Switch A = NONE
Candidates = ONOS 2, ONOS 3
Master
Switch A = NONE
Candidates = ONOS 2, ONOS 3
Master
Switch A = ONOS 2
Candidates = ONOS 3
Master
Switch A = ONOS 2
Candidates = ONOS 3
Master
Switch A = ONOS 2
Candidates = ONOS 3
Notes: Switch A is being controlled by Instance 1 and the registry shows it as master for switch A.
Instance 1 has a failure and dies.
Registry detects that instance 1 is down and release the mastership for Switch A.
Remaining candidates join the mastership election within registry. Lets say Instance 2 wins the election and is marked in registry as the master for Switch A.
The channel with Instance 2 becomes the active channel and other channel becomes passive.
This enables a quick failover of switch when there is a control plane failure.
----- Meeting Notes (7/29/13 12:57) -----
Mention strong consistency and elegent coordination

## Slide 17: Network Graph

## Slide 18: ONOS Network Graph Abstraction
Cassandra Key/Value Store
Id: 1
A
Id: 101, Label
Id: 103, Label
Id: 2
C
Id: 3
B
Id: 102, Label
Id: 104, Label
Id: 106, Label
Id: 105, Label
Network Graph
Titan Graph DB
Notes: Network graph is organized as a graph database. Vertices as network objects and connected by edges as relation between the vertices.
We use Titan as graph DB with Cassandra as its backend.
Cassandra is eventually consistent

## Slide 19: Network Graph
port
switch
port
device
port
on
port
port
port
link
switch
on
device
host
host
Network state is naturally represented as a graph
Graph has basic network objects like switch, port, device and links
Application writes to this graph & programs the data plane
Notes: Network is naturally a graph with switches, ports, devices as objects as vertices. Similarly links and attachment points are modeled as edges.
Applications can traverse and write to this graph to program the data plane.
How? Lets look at this example application

## Slide 20: Example: Path Computation App on Network Graph
port
switch
port
device
Flow path
Flow entry
port
on
port
port
port
link
switch
inport
on
Flow entry
device
outport
switch
switch
host
host
flow
flow
Application computes path by traversing the links from source to destination
Application writes each flow entry for the path
Thus path computation app does not need to worry about topology maintenance
Notes: Path Computation is an application which is using Network Graph.
The application can find a path from source to destination by traversing links and program this path with flow entries to create a flow-path.
These flow-entries are translated by ONOS core into flow table rules and pushed onto the topology.
Last bullet: Application is made simple and stateless. It does not need to worry about topology maintenance.
----- Meeting Notes (5/14/13 14:16) -----
start without text. Bring in text at end and make one point

## Slide 21: Example: A simpler abstraction on network graph?
Logical Crossbar
port
switch
port
device
Edge Port
port
on
port
port
port
link
switch
physical
on
Edge Port
device
physical
host
host
App or service on top of ONOS
Maintains mapping from simpler to complex
Thus makes applications even simpler and enables new abstractions
Virtual network objects
Real network objects
Notes: Network graph simplifies applications but can it be used to accelerate innovations of simpler abstractions in control plane?
Here is an example of Logical Crossbar. The complexity of network state and topology is hidden.
One can build hierarchy of these abstractions further hiding the complexity.
Last bullet: We feel network graph will unlock innovations.
7 minute Marker

## Slide 22: Network Graph and Switches
Switch Manager
Switch Manager
Switch Manager
Network Graph: Switches
OF
OF
OF
OF
OF
OF
Notes: Let us see how ONOS builds the network graph. Each ONOS node has a switch manager. When switches connect, switches and ports are get added as switches register with an ONOS node. When switches disconnect, they get marked as inactive in the network graph.

## Slide 23: Network Graph and Link Discovery
SM
Network Graph: Links
SM
SM
Link Discovery
Link Discovery
Link Discovery
LLDP
LLDP
Notes: Each node sends out LLDP on the switches connected to it. Links with source and destination port controlled by different ONOS nodes can also be discovered using the network graph.

## Slide 24: Devices and Network Graph
Network Graph: Devices
SM
SM
SM
LD
LD
LD
Device Manager
Device Manager
Device Manager
PKTIN
PKTIN
PKTIN
Host
Host
Host
Notes: Host packet Ins are used to learn about devices, their attachment points. The network graph is updated with this information.

## Slide 25: Path Computation with Network Graph
SM
SM
SM
LD
LD
LD
Host
Host
Host
DM
DM
DM
Path Computation
Path Computation
Path Computation
Network Graph: Flow Paths
Flow 1
Flow 4
Flow 7
Flow 2
Flow 5
Flow 3
Flow 6
Flow 8
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Notes: Flow paths are provisioned in ONOS.
The source dpid of a flow is used to partition which node will compute the path. Computed paths and flow entries are also stored in the network graph.
Flow entries have relationship to the switches.

## Slide 26: Network Graph and Flow Manager
SM
SM
SM
LD
LD
LD
Host
Host
Host
DM
DM
DM
Flow Manager
Network Graph: Flows
Flow Manager
Flow Manager
Flowmod
Flowmod
Flowmod
Flow 1
Flow 4
Flow 7
Flow 2
Flow 5
Flow 3
Flow 6
Flow 8
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Flow entries
Path Computation
Path Computation
Path Computation
Notes: Each flow manager programs the switches connected to it using the state in the network graph.
When a link fails, PC will recompute a new path and Flow Manager will push new flow entries.

## Slide 27: ONOS High Level Architecture
Host
Host
Host
Titan Graph DB
Cassandra In-Memory DHT
Instance 1
Instance 2
Instance 3
Network Graph Eventually consistent
Distributed Registry Strongly Consistent
Zookeeper
OpenFlow Controller+
OpenFlow Controller+
OpenFlow Controller+
+Floodlight Drivers
Scale-out
Coordination
Distributed Network
Graph/State
Control Application
Control Application
Applications
Notes: Built on two distributed data constructs
1> Network Graph which is the global network view containing the network state represented as a graph which is eventually consistent
2> Distributed Registry is the global cluster management state stored in Zookeeper using transactional consistency.
Multiple instances of ONOS control different parts of network and help realize a single global network view by cooperatively using these two distributed data constructs.
----- Meeting Notes (5/15/13 14:21) -----
Distribruted Registry keeps information on who is in control of the switch objects and has write permissions to update the network graph. In general it stores the resource ownership in a strongly consistent way.
----- Meeting Notes (7/29/13 12:57) -----
order animation
remove floodlight

## Slide 28: Reflections/Lessons Learned: Things we got right
Control isolation (sharding)
  Divide network into parts and control them exclusively
  Load balancing -> we can do more
Distributed data store
  That scales with controller nodes with HA -> though we need low latency distributed data store
Dynamic controller assignment to parts of network
  Dynamically assign which part of network is controlled by which controller instance -> we can do better with sophisticated algorithms
Graph abstraction of network state
  Easy to visualize and correlate with topology
  Enables several standard graph algorithms
Notes: ----- Meeting Notes (11/20/13 23:20) -----
We got few things right. Partitioning the network into parts to be controlled exclusively helps in basic load balancing. And ofcourse we could do better.
Scalability and HA was weill handled using distributed data stores.
Dynamic fail-over and assignment of part of network to controller helps very well in HA. We could have done better using sophisticated algorithms.
Network Graph as northbound abstraction is appealing to many and we can do better by formalizing a graph model for ONOS.

## Slide 29: Reflections/Lessons Learned: Limitations
Performance
  Several layers of open source sw means lower performance
  Very little visibility under-the-hood
  Different types of network state treated the same way
Debuggability
  Debugging for performance as well as correctness is difficult due to lack of visibility
  Cannot customize to our needs
  Heavyweight building blocks
Spectrum of use cases
  Routing, TE, and BGP are the only use cases tried – need more
Features
  Meant to be a prototype and so didn’t consider config, measurements, …
Notes: ----- Meeting Notes (11/20/13 17:49) -----
Limitations:
1> Performance
2> Debuggability
3> Lack of use cases
4> several features are miissing
Next phase:
architectural directions
1> state usage pattern
2> control over sharding
3> Customizing to data model to our sharding (Maximize local reads/writes)
3> Using lean and high perfomance open source
4> Engaging network providers and vendors for use cases
----- Meeting Notes (11/20/13 23:20) -----
ONOS has few limitations
First we have several features missing and as we learn we will add them.
Open source tools are good for rapid prototype but do not help in customizng to our performance needs.
While designing and developing we lacked several use cases and may have incorrect assumptions on network state. Now we are investigating different types of network states and their usage patterns.
Debugging ONOS is not easy due to lack of visibility of open source tools under-the-hood.

## Slide 30: Next Phase: Architectural Directions
Optimize for different types of network state
  Identify different types of network state and usage patterns
  Quantify the requirements for each type of state
  Understand the performance needs and strategize for optimal usage
Control over sharding
  Optimize for different types of network states
  Lockless concurrent operations on network state
Customize our data model to our sharding
  Maximize local reads/writes
  Reduce need for remote read/writes as far as possible
Use lean and high performance open source if possible
  For example reduce dependency on general purpose open source DHT
Engage network providers and vendors
  Feature set and use cases
Notes: Started in December with a primary goal to demonstrate we can build ONOS with scale-out distributed architecture which has high-availability and global network view as network graph.
----- Meeting Notes (11/20/13 17:33) -----
drop the non-goals
demonstrate service provider use cases

## Slide 31: ONOS: Many Challenges Ahead …
Goal: Functionality with performance, visibility, customization
Modular building blocks
  Swap-in and out with commercial or different open-source components
  Low latency distributed data store and state synchronization
  Low latency events and notifications
Distributed state management
  Choice of consistency models for different network state
  CAP theorem implications on applications programming
Sharding and replication of network state
  Optimize handling different types of network states (replicate/shard)
  Optimize data models for our purpose
  Lockless concurrent operation on the network states
Northbound Abstraction
  Network Graph API for applications
Hierarchical control - Recursive SDN (with Berkeley)
Notes: ----- Meeting Notes (11/20/13 17:49) -----
hierarchical control plane at the end
combine under
-> Modular building blocks
-> Distributed state management
-> Sharding and repllication
-> Northbound abstraction

## Slide 32: ONOS Open Source Initiative … stay tuned…

## Slide 33: onos.onlab.us
Pankaj Berde
Masayoshi Kobayashi
Brian O’Conner
Rachel Sverdlov
Naoki Shiota
William Snow
Pavlin Radoslavov
Jonathan Hart
Pingping Lin
Suibin Zhang
Yuta Higuchi
Guru Parulkar
The ONOS team:
Notes: In this demo we will create isolated virtual networks, each with their own topology. Each virtual network is connected to its own network operating system. Finally, we show demonstrate the resiliency features of OVX.